## Slide 1
HM11 C41AB/C43AB/C46AB
I2C REG dump tool
2026/06/01

## Slide 2: Preparation the input file ( Two ways - One )
Execute the corresponding BMC command to obtain the I2C dump log.
  i2cdump -y -f 15 0x60 (DC-SCM)
  i2cdump -y -f 6 0x30 (Global FPGA)
  i2cdump -y -f 5 0x30 (HPM FPGA1)
  i2cdump -y -f 5 0x31 (HPM FPGA2)
Save the output as a text file (log file).
Rename the files using the following naming convention:
  SLEDy_xxx_scm_cpld
  SLEDy_xxx_cpld1
  SLEDy_xxx_cpld2
  SLEDy_xxx_glb
  Note : xxx can be any user-defined prefix.
  SLEDy indicates the sled number, where y = 1, 2, 3, or 4.
The order is flexible. As long as the filename contains the corresponding keywords (such as SLEDy, scm_cpld, cpld1, cpld2, or glb), the parser can identify the file correctly.

## Slide 3: Preparation the input file ( Two ways - Two )
Execute the corresponding BMC command to obtain the I2C dump log.
  i2cdump -y -f 15 0x60 (DC-SCM)
  i2cdump -y -f 6 0x30 (Global FPGA)
  i2cdump -y -f 5 0x30 (HPM FPGA1)
  i2cdump -y -f 5 0x31 (HPM FPGA2)
Save the all output as a same text file (log file).
Rename the files using the following naming convention
  xxx_i2cdump
And the content format should also be adjusted and organized by SLED, as shown below

## Slide 4
The command
I2C dump content
Grouped by SLED (e.g., SLED1, SLED2, SLED3, SLED4)

## Slide 5: Sample file
Two ways - Two
Two ways - One

## Slide 6: Put the log / txt file into the log_input file
Two output file formats will be generated. 1. Select either output file. 2. Copy the selected file into the log_input directory.

## Slide 7: Click the execute result.bat
1. Click the execute result.bat

## Slide 8: Enable or disable the PASS log output (based on your requirements)

## Slide 9: Next step
Linux Shell script to auto dump and transfer the .txt into Windows